KB ENTERPRISE, CORP.

199 Landfill RD

PO BOX 1278

Anaconda, MT 59711

406-563-9166

406-563-3467 Fax

INSULATED PIPE SUPPORTS

SNAPPITZ

PVC – Urethane self locking pipe support system

| CLAMP SIZE | Insulation & Jacketing Length |
| --- | --- |
| Copper Pipe Size | Iron Pipe Size | Iron Pipe Outside Diameter |  | 1/2" | 1" | 1 1/2" | 2" | 2 1/2" | 4" | 6" |
| 7/8” | 1/2" | .840 |  | 1.900 | 2.875 | 4.000 | 5.000 | - | 4 | - |
| 1-1/8” | 3/4" | 1.050 |  | 2.375 | 2.875 | 4.000 | 5.000 | - | 4 | - |
| 1-3/8” | 1" | 1.315 |  | 2.375 | 3.500 | 4.500 | 5.563 | - | 4 | - |
| 1-5/8” | 1 1/4" | 1.660 |  | 2.875 | 3.500 | 5.000 | 5.563 | - | 4 | - |
| 2-1/8” | 1 1/2" | 1.900 |  | 3.500 | 4.000 | 5.000 | 6.625 | - | 4 | - |
| 2-5/8” | 2" | 2.375 |  | 3.500 | 4.500 | 5.563 | 6.625 | 7.625 | 4 | - |
| 3-1/8” | 2 1/2" | 2.875 |  | 4.000 | 5.000 | 6.625 | 7.625 | 8.625 |  | 6 |
|  | 3" | 3.500 |  | 4.500 | 5.563 | 6.625 | 7.625 | 8.625 |  | 6 |
|  | 3 1/2" | 4.000 |  | 5.000 | 6.625 | 7.625 | 8.625 | 9.625 |  | 6 |
| 4-1/8” | 4" | 4.500 |  | 5.563 | 6.625 | 7.625 | 8.625 | 9.625 |  | 6 |
|  | 4 1/2" | 5.000 |  | 6.625 | 7.625 | 8.625 | 9.625 | 10.750 |  | 6 |
|  | 5" | 5.563 |  | 6.625 | 7.625 | 8.625 | 9.625 | 10.750 |  | 6 |

Up to 2 ½” pipe, Trymer has adequate compressive strength to meet

the requirements of weight bearing loads at the hanger point.

PVC pipe has the following smoke & flame characteristics when tested in

accordance with ASTM E84-05:

Flame spread classification: 5      Smoke developed classification: 30

Standard size is 4” length of insulation and jacketing for pipes ½” – 2”.

6” length jacketing & insulation is used for pipes 2 ½” – 6”.

Trymer 2000 - Urethane has the following characteristics:

- Compressive Strength = 24 p.s.i. average

- Flexural Strength = 44 p.s.i. average

- K Factor = .190 @ 75 degree F - aged 180 days

- Working Temperature Range = -297 degree F to +300 degree F

- Trymer 2000 insulation is used for 1/2 inch wall thickness insulation inserts

Please visit us at our website: www.snappitz.com

# Text boxes

Insulation OD